## Slide 1: Nuclear Thermal Propulsion at The Ohio State University
Noah Gula (gula.8@osu.edu)
April 13, 2021

## Slide 2: Presentation Overview
A brief history of nuclear thermal propulsion.
  When did it all start?
  Project Rover and NERVA
  Cancelling NERVA
  Isn’t NTP dead?
How exactly does NTP work?
  What are the governing equations and principles?
  How does it stack up against other forms of propulsion?
  What are the challenges associated with NTP?
  What are we doing at OSU to deal with them?
NTP at OSU

## Slide 3: A Brief History of Nuclear Thermal Propulsion

## Slide 4: When did it all start?
Originally, NTP was first developed for aircraft by the US Army Air Forces in 1946.
The goal was to develop an aircraft which used nuclear thermal energy to heat air as it passed through the engines.
An aircraft carrying a nuclear reactor was flown 47 times, but the reactor never powered the aircraft.
The program was eventually cancelled in 1961 by JFK.
NTP at OSU
[1] Los Alamos National Laboratory, http://www.lanl.gov/newsroom/photo/history.php
Notes: Pictured is a Kiwi Prime A nuclear reactor on the test stand at the Atomic Energy Commission’s Nevada Test Site.

## Slide 5: Project Rover and NERVA
Project Rover intended to build a nuclear-powered stage for an ICBM, started in 1955 by Los Alamos Scientific Laboratory.
When NASA was created in 1958, it partnered with the Atomic Energy Commission (now the Department of Energy) to manage the project.
The program produced three different types of reactors, all using Highly Enriched Uranium (HEU).
By 1957, a nuclear upper stage was no longer needed. But something else came up that increased interest in NTP...
Eventually, the project transformed into the Nuclear Engine for Rocket Vehicle Application (NERVA) in 1961.
In all, NERVA was tested six times between 1964-1969 before being cancelled.
NTP at OSU
[2] Department of Energy, https://web.archive.org/web/http://www.nv.doe.gov/library/photos/photodetails.aspx?ID=824
Notes: Pictured is the NERVA XE in Engine Test Stand-1. The two technicians at the bottom right provide a sense of scale.
In 1957, the Soviet Union launched Sputnik-1, leading to the creation of NASA.

## Slide 6: Cancelling NERVA
By 1970, a battle between Congress and Pres. Nixon emerged.
Nixon repeatedly tried to cancel NERVA, but Congress continued to (inadequately) fund the project through 1972.
Concerns by Congress and the public grew over the safety of NTP.
In early 1973, NASA announced the program was cancelled.
After 17 years, $8.81B was spent (in 2021 USD). Biden recently proposed a $24.7B budget for NASA in 2022.
NTP at OSU
Notes: Chart shows the “crash program” of NASA during the Apollo era. Data from congressional appropriations bills, visualization my own.

## Slide 7: I thought NTP was “dead”?
NTP at OSU
https://spacenews.com/general-atomics-wins-darpa-contract-to-design-nuclear-reactor-to-power-missions-to-the-moon/
https://spacenews.com/momentum-grows-for-nuclear-thermal-propulsion/
https://spacenews.com/report-recommends-nasa-accelerate-space-nuclear-propulsion-development/
https://spacenews.com/administration-policies-seek-to-promote-use-of-space-nuclear-power/
https://spacenews.com/white-house-releases-space-nuclear-power-strategy/
Notes: Just a handful of recent articles discussing the future of NTP.

## Slide 8: How exactly does Nuclear Thermal Propulsion work?

## Slide 9: NTP Operation
NTP at OSU
Hydrogen Tank
Nozzle
Pump
Turbine
~60%
~40%
Core

## Slide 10: Fundamental Governing Equation
NTP at OSU
Chamber Temperature
(big is good)
Chamber Pressure
(big is good)
Propellant Molar Mass
(small is good)
H2: 1 g/mol
CO2: 44 g/mol
H2O: 18 g/mol
To increase performance, we need high temperature and high strength materials!

## Slide 11: How does NTP compare to chemical?
NTP is comparable to other types of chemical propulsion (including solid and liquid).
It enjoys a much higher efficiency (specific impulse) while still achieving a similar thrust to weight ratio.
Best application is for in-space propulsion.
Thanks to its higher specific impulse, NTP is a viable candidate for human spaceflight missions to Mars.
NTP at OSU
Chart: Comparison of Selected Propulsion Types [3]
| 0.1 | 100
Chemical | 200 | 469
Liquid monoprop | 194 | 223
Plasma | 700 | 2500
Ion | 1310 | 7650
Solar Thermal | 400 | 700
Nuclear Thermal | 850 | 1000

## Slide 12: NTP Operation
NTP at OSU
Hydrogen Tank
Nozzle
Pump
Turbine
~60%
~40%
Core
Tie Tube

## Slide 13: Cross-Section of the NERVA Core [4]
NTP at OSU

## Slide 14: Tie Tube Detail
In the NERVA HEU reactor core, each tie tube is surrounded by six fuel elements.
It servers three purposes:
  To provide structural integrity to the core
  To increase the enthalpy of the hydrogen before it goes to the turbine, and
  To provide some amount of neutronic moderation.
Hydrogen flows through the inner tie tube, turns around at the bottom, and flows back up through the outer tie tube.
NTP at OSU
[5]

## Slide 15: How is NTP different than chemical?
In a chemical rocket engine, when you stop the flow of propellant, the combustion stops.
When the combustion stops, the generation of heat in the engine stops.
In NTP, a nuclear reactor continues to emit “decay heat” for a long time after it is “turned off.”
If this decay heat is not delt with, the engine will melt.
NTP at OSU

## Slide 16: So how do you deal with the decay heat?
You must continue flowing hydrogen through the tie tubes in order to carry the decay heat away.
But it doesn’t all have to be wasted!
  Instead of dumping overboard, make it a closed loop and use it to generate electricity (J. Clark, J. Plank)
  It can still go through the nozzle and therefore contributes to thrust (D. Scott, J. Plank)
How do you know what amount of hydrogen is required to maintain the integrity of the engine? (J. Plank, N. Gula)
NTP at OSU
NASA. https://www.nasa.gov/centers/glenn/images/content/101877main_BNTR_concept_516x266.jpg

## Slide 17: Use of real-time simulations [4]
To optimize the propellant flow rate, we want to find the minimum mass flow which maintains the moderator temperature below 800 K.
This is accomplished by using real-time simulations (in Ansys, Simulink, etc.).
The temperature of the core, hydrogen pressure, and current mass flow rate are supplied as boundary conditions, and the model tries to figure out what the minimum flow rate is required.
NTP at OSU

## Slide 18: Use of real-time simulations [4]
To optimize the propellant flow rate, we want to find the minimum mass flow which maintains the moderator temperature below 800 K.
This is accomplished by using real-time simulations (in Ansys, Simulink, etc.).
The temperature of the core, hydrogen pressure, and current mass flow rate are supplied as boundary conditions, and the model tries to figure out what the minimum flow rate is required.
NTP at OSU

## Slide 19: Use of real-time simulations [4]
Jack Plank performed computational simulations and found that up to forty percent of hydrogen could be saved in the cool-down phase (!!!)
But how do we know that the computational model behaved correctly? We need experimental results.
NTP at OSU

## Slide 20: Test Stand P&ID
NTP at OSU
Nitrogen Supply Tank
Pressure Regulator
Manual “Run” Valve
Mass Flow Controller
Upstream Flow Conditions (Pressure + Temperature)
Tie Tube & Heat Sink
Test Article Thermocouples
Downstream Flow Conditions (Pressure + Temperature)
Optional Orifice
Optional Exhaust Nozzle

## Slide 21: Test Article Design
NTP at OSU

## Slide 22: Test Article Design
NTP at OSU

## Slide 23: Cap and Graphite Filler Structure
NTP at OSU

## Slide 24: Data Acquisition and Control System
NTP at OSU
Arduino Mega (2560 R3)
Data Acquisition
Arduino Uno (R3)
Controller
Lab Computer with Python/MATLAB
Data/Command Processing

## Slide 25: Control System Cycle
Arduino Mega collects test article data
Arduino Uno sends mass flow command
Test article responds to new conditions
Simscape/Ansys determines optimal mass flow rate
Serial port sends data
Serial port sends command
NTP at OSU

## Slide 26: Control System Overview
NTP at OSU
Arduino Uno (R3)
Controller
Nitrogen tank
FT
Test article
Heater controller

## Slide 27: Questions?

## Slide 28: Extra Slides

## Slide 29: Other OSU Efforts
Is there a better regen channel geometry which allows hotter chamber temperatures? (N. Salamon)
  Can we realize this in an additively manufactured prototype? (K. Melendez et al.)
Is dead reckoning a viable navigational method for NTP burns (J. D. Kostik et al., A. Montanez et al.)
NTP at OSU

## Slide 30: Tie Tube and Fuel Element Cross Section
NTP at OSU
[6]

## Slide 31: HALEU Inverted SNRE
NTP at OSU

## Slide 32: Reference
[1] Unless otherwise indicated, this information has been authored by an employee or employees of the Los Alamos National Security, LLC (LANS), operator of the Los Alamos National Laboratory under Contract No. DE-AC52-06NA25396 with the U.S. Department of Energy. The U.S. Government has rights to use, reproduce, and distribute this information. The public may copy and use this information without charge, provided that this Notice and any statement of authorship are reproduced on all copies. Neither the Government nor LANS makes any warranty, express or implied, or assumes any liability or responsibility for the use of this information.
[2] Photo courtesy of National Nuclear Security Administration / Nevada Field Office
[3] G. P. Sutton, O. Biblarz (2017) Rocket Propulsion Elements, 9th Ed. Wiley
[4] J. Plank (2021) Nuclear Thermal Propulsion Cool-Down Phase Optimization Through Quasi-Steady Computational Analysis, and the Effect of Auxiliary Heat Removal Systems. Ohio State University
[5] F. P. Durham (1979) Nuclear Engine Definition Study Preliminary Report Volume I – Engine Description. Los Alamos Scientific Laboratory
[6] Fittje, J. E., Borowski, & S. K., Schnitzler, B. (2015) Revised Point of Departure Design Options for Nuclear Thermal Propulsion. AIAA.
NTP at OSU